## Slide 1: ROBOT SIMULATION

## Slide 2: Table of content
Methods of robot programming
Simulation concept
Off-line programming
advantages of offline programming.

## Slide 3: Introduction
Robot simulation is an essential tool in every roboticist's toolbox.
The term robotics simulator can refer to several different robotics simulation applications. For example, in mobile robotics applications, behavior-based robotics simulators allow users to create simple worlds of rigid objects and light sources and to program robots to interact with these worlds.
One of the most popular applications for robotics simulators is for 3D modeling and rendering of a robot and its environment.
This type of robotics software has a simulator that is a virtual robot, which is capable of emulating the motion of an actual robot in a real work envelope.
The use of a robotics simulator for development of a robotics control program is highly recommended regardless of whether an actual robot is available or not.
The simulator allows for robotics programs to be conveniently written and debugged off-line with the final version of the program tested on an actual robot. This primarily holds for industrial robotic applications only, since the success of off-line programming depends on how similar the real environment of the robot is to the simulated environment.

## Slide 4: Conti…
Sensor-based robot actions are much more difficult to simulate and/or to program off-line, since the robot motion depends on the instantaneous sensor readings in the real world.
Among the newest technologies available today for programming are those which use a virtual simulation.
Simulations with the use of virtual models of the working environment and the robots themselves can offer advantages to both the company and programmer.
By using a simulation, costs are reduced, and robots can be programmed off-line which eliminates any down-time for an assembly line.
Robot actions and assembly parts can be visualised in a 3-dimensional virtual environment months before prototypes are even produced.
Writing code for a simulation is also easier than writing code for a physical robot.
While the move toward virtual simulations for programming robots is a step forward in user interface design, many such applications are only in their infancy.

## Slide 5: ROBOT PROGRAMMING
Typically performed using one of the following
– On line
• lead through programming
– Off line
• robot programming languages
• task level programming

## Slide 6: Robot Programming Methods
• Offline:
– write a program using a text-based robot programming language
– does not need access to the robot until its final testing and implementation
• On-line:
– Use the robot to generate the program
• Teaching/guiding the robot through a sequence of motions that can them be executed repeatedly
• Combination Programming:
– Often programming is a combination of on-line and off-line
• on-line to teach locations in space
• off-line to define the task or “sequence of operations"

## Slide 7: Methods of robot programming
Robot Programming is the defining of desired motions so that the robot may perform them without human intervention.
Identifying and specifying the robot configurations (i.e. the pose of the end-effector, with respect to the base-frame)
  Manual method
  Walkthrough method-Teaching physically
  Lead through method- Teach pendant
  Off-line programming

## Slide 8: Type of Robot Programming
Joint level programming
– basic actions are positions (and possibly movements) of the individual joints of the robot arm: joint angles in the case of rotational joints and linear positions in the case of linear or prismatic joints.
Robot-level programming
– the basic actions are positions and orientations (and perhaps trajectories) and the frame of reference attached to it.
High-level programming
– Object-level programming
– Task-level programming

## Slide 9: Online Programming
On line programming takes place at the site of production itself and involves the workcell.
Online programming system uses a ‘teach pendant’ to direct the robot’s movement which allows trained personnel physically to lead the robot through the desired sequence of events by activating the appropriate pendant button or switch.
Online programming is a convenient and easy method of programming when tasks are simple and revisions or adjustments can be made on the spot.

## Slide 10: Use of Teach Pendant
• hand held device with switches used to control the robot motions
• End points are recorded in controller memory
• sequentially played back to execute robot actions
• trajectory determined by robot controller
• suited for point to point control applications

## Slide 12: Lead Through Programming
Lead through programming requires the operator to move the robot arm through the desired motion path during a teach procedure, thereby entering the program into the controller memory for subsequent playback.

## Slide 13
• Advantage:
– Easy
– No special programming skills or training
• Disadvantages:
– not practical for large or heavy robots
– High accuracy and straight-line movements are difficult to achieve, as are any other kind of geometrically defined trajectory, such as circular arcs, etc.
difficult to edit out unwanted operator moves
difficult to incorporate external sensor data
Synchronization with other machines or equipment in the work cell is difficult
A large amount of memory is required
Requires access to the robot
Programs exist only in the memory of robot control system – often difficult to transfer, document, maintain, modify
Easy to use, no special programming skills required
Useful when programming robots for wide range of repetitive tasks for long production runs
RAPID

## Slide 14: Walk-Through programming or teaching
In walk through programming, the teacher physically moves the robot through the desired positions with in the robot’s working envelope.
The robot controller may scan and store coordinates values on a fixed-time interval basis.
These values and other functional information are replayed in the automatic mode.

## Slide 15: Off-line programming
Programs can be developed without needing to use the robot
The sequence of operations and robot movements can be optimized or easily improved
Previously developed and tested procedures and subroutines can be used
External sensor data can be incorporated, though this typically makes the programs more complicated, and so more difficult to modify and maintain
Existing CAD data can be incorporated-the dimensions of parts and the geometric relationships between them, for example.
Programs can be tested and evaluated using simulation techniques, though this can never remove the need to do final testing of the program using the real robot
Programs can more easily be maintained and modified
Programs can more be easily properly documented and commented.

## Slide 17: A ROBOT WORK CELL
A Robot and its associated equipment form a basic robot work cell (or Work Station).
Some times human workers can also be included in the work cell to perform tasks that are not easily automated.
These tasks may consists of inspection operation or operations that require judgment or a sense of touch that robot do not process.
•Two aspects arise in the robot applications in industrial production line:
i. One related to the design of robot work cell which may consists of more than one robot and more than one machine.
ii. The other is related to control system that will coordinate the activities among various components of work cell